## Slide 1: Boundary Helps: Efficient Routing Protocol using Directional Antennas in Cognitive Radio Networks
Ying Dai and Jie Wu
Computer and Information Sciences
Temple University

## Slide 2: Roadmap
Introduction
Problem Formulation
Boundary Nodes
Piggyback
Route Selection
Simulation
Extensions
Conclusion

## Slide 3: 1. Introduction
A real life scenario:
  Privileged User
  Road blocked
  Avoid in advance?

## Slide 4: Cognitive Radio Networks
Similar situation in Cognitive Radio Networks (CRNs):
Primary User
Secondary User
A
B
channel m
PU
channel m
x

## Slide 5: Intuition
Primary users’ (PUs’) activities are unpredictable.
Routes selected by traditional algorithms are unreliable.
Q: What if we can select routes that avoid those “restricted areas” in advance?

## Slide 6: Intuition
Answer : Make use of boundary nodes.
Also, we need the help of directional antennas.
Benefits: 1) tell the direction of PUs; 2) increase the space reuse ratio.
PU
channel m
A
Traffic Blocker!

## Slide 7: 2. Problem Formulation
Objective: Route selection
  Delay
  Reliability
  SINR requirements of PUs and SUs
Unpredictable PUs’ activities
No optimal solution
We propose an efficient solution, with the help of boundary nodes!

## Slide 8: 3. Boundary Nodes
How does a node know if it is a boundary node itself?
Answer: By the variance of its sensing results in different directions!
We use USRPs to show the properties of a boundary node.
  USRP: Universal Software Radio Peripheral

## Slide 9: 3. Boundary Nodes
5 USRP N200s
  One PU; Others simulate a four-directional SU.
  Central frequency: 1.3005GHz

## Slide 10: 3. Boundary Nodes
Sector I: -50dB; Sector II: -87dB

## Slide 11: Routing Overview
Overview:
  Route Discovery;
  Piggyback;
  Route Selection
S
D
A
B
M
N

## Slide 12: 4. Piggyback
Route discovery : traditional ways
Piggyback: What kind of information?
Non Boundary Node:
(IN, OUT, -, -)
A
I
II
III
IV
data
A: (I, III, -, -)
Boundary Node:
(IN, OUT, m, μ)
PU
channel m
B
I
II
III
IV
C
I
II
III
IV
data
data
B: (I, II, m, 1)
C: (IV, II, m, 0)
μ = 1: ENTER
μ = 0: EXIT

## Slide 13: Link Information
Based on piggyback information, for a link, we can know:
  If the link is inside or outside a PU area;
  How many PU areas the link is located inside.
  Then, we define the link length based on the above information.
  A larger value for link length will show that the link is within more PU areas.

## Slide 14: Four Cases
Four cases to identify if a link (AB) is within a PU area, given the piggyback information:
PU
channel m
Case1: Neither A nor B is a boundary node, but the closest boundary node on the route indicates the entering into a PU area.
C: (I, III, m, 1)
A: (I, II, -, -)
B: (IV, II, -, -)
A
I
II
III
IV
data
B
I
II
III
IV
C
I
II
III
IV

## Slide 15: Four Cases
PU
channel m
Case2: A is a boundary node and B is not. In addition, A indicates the entering into a PU area.
A: (I, II, m, 1)
B: (IV, II, -, -)
A
I
II
III
IV
data
B
I
II
III
IV

## Slide 16: Four Cases
PU
channel m
Case3: B is a boundary node and A is not. In addition, B indicates the exiting from a PU area.
A: (I, II, -, -)
B: (IV, II, m, 0)
A
I
II
III
IV
data
B
I
II
III
IV

## Slide 17: Four Cases
PU
channel m
Case4: Both A and B are boundary nodes. In addition, A indicates the entering into a PU area and B indicates the exiting from the PU area.
A: (I, II, m, 1)
B: (I, III, m, 0)
A
I
II
III
IV
data
B
I
II
III
IV

## Slide 18: Special Case
II
IV
channel m1
A
Special case: if a link is within multiple PU areas, we can still detect it.
M: (IV, II, m2, 1)
N: (IV, II, m1, 1)
A: (IV, II, -, -)
B: (IV, III, -, -)
channel m2
PU
PU
B
I
III
M
I
II
III
IV
N
I
II
III
IV
data
The previous boundary nodes both have μ = 1.
Link AB are in two PU areas, occupying m1 and m2 when active.
II
IV
I
III

## Slide 19: 5. Route Selection
Intuitively, we can select the route:
  with less links that pass through a PU area;
  with less links that are within multiple PU areas.
We need to define the route length!

## Slide 20: Link Length
First, we define the length of link AB, denoted as (LAB):
  LAB = 1, if link AB is not in any of the PUs’ areas;
  LAB = |M|/(|M| - C(m)), if AB is within the PUs’ areas.
    |M| is the total number of channels in the network;
    C(m) is the counter of how many PU areas AB is in.

## Slide 21: Route Length
The route length is defined as the sum of the link length on the route: Σ(LAB)
  The route with more links in a PU area will have a larger value of route length.
  The route that passes through more PU areas will have a larger value for route length.

## Slide 22: Route Length
An example:
Route R’ has more links in the PU area.
Some links of R’ are in multiple PU areas.
These properties can be shown by the value of route length.

## Slide 23: Route Length
Calculate route length:
The route with smaller route length will be chosen.
  In this example, R will be chosen since 7< 19/2.

## Slide 24: Supplementary Information
Our route length calculation is based on the simplified SINR model:
  It aims at showing the influence of PU areas;
  It can also be easily extended to other routing algorithms using real SINR models.
Our model also assumes the accuracy of boundary node detections:
  It can be extended to consider the misdetection of boundary nodes.

## Slide 25: 6. Simulation
Simulation Settings
  Network Area: 2,000 X 2,000
  Number of nodes: [100, 300]; Approximate range: [30, 50]; Number of channels:[10, 25];
  Number of PUs: [10, 50]; Operation range of each PU: [300, 500]; Active probability: 0.5
  Number of sectors: 4; Delay for one channel switch: 0.1s.

## Slide 26: 6. Simulation
Simulation Results
  Performance metrics: average number of channel switches.

## Slide 27: 6. Simulation
Simulation Results
  Performance metrics: total delay

## Slide 28
Missing boundary node
PU
channel m
Neither A nor B is a boundary node.
A
I
II
III
IV
data
B
I
II
III
IV
However, by the sensing result variance, we can detect the entering of the PU area.
Like a virtual boundary node..
V
7. Extension1 – Imperfect Information

## Slide 29: 7. Extension2 – Imperfect Information
Imperfect Information
PU
channel m
A
I
II
III
IV
data
B
I
II
III
IV
Link AB located at the boundary area.
Whether to count link AB as in the PU area is decided by a predefined threshold.

## Slide 30: 7. Conclusion
Directional antenna + boundary nodes.
Detect if a link is outside PU areas, inside a single PU area, or inside multiple PU areas.
Define the link length and route length.
Our algorithm can be easily applied or extended in other models.

## Slide 31
Thank you!