## Slide 1: Multi-Path-Based Avoidance Routing in Wireless Networks
Kazuya Sakai, Min-Te Sun, Wei-Shinn Ku, Jie Wu, and Ten H Lai
Tokyo Metropolitan University, National Central University, Auburn University, Temple University, The Ohio State University
ksakai@tmu.ac.jp
July 2nd, 2015

## Slide 2: Outline
Introduction to avoidance routing
The Problem Formulation
Multi-Path Based Avoidance Routing (MPAR)
Performance Evaluation
Conclusions

## Slide 3: 1. Introduction
We are interested in designing a secure routing protocol in ad hoc networks
Cryptographic operations can protect end-to-end communications
Two issues
  Computing power are more and more accessible and inexpensive, i.e., encryption is no longer a perfect solution
  Software implementations of cryptographic protocols may be seriously flawed (e.g., generating prime numbers)
Avoidance routing
  Avoiding insecure areas is the primary countermeasure against potential adversaries

## Slide 4: Avoidance and Multi-Path
What is “avoidance” in ad hoc routing?
  Motivations for non-shortest path routing
  Load balancing, energy-aware, congested links, etc.
How to utilize “multi-path”?
  Improving throughput by parallelizing message transmissions
  Fault tolerance, e.g., backup paths
Our definition
  A routing path physically avoids insecure areas
  e.g., malicious countries, compromised nodes, etc.
  We utilize the idea of multi-path with the XOR coding in a very different way

## Slide 5: Avoidance Routing
The avoidance routing problem
  Avoid insecure area that adversaries can eavesdrop on communications
Fig. An insecure area in a graph
An insecure area

## Slide 6: 2. The Problem Formulation
Introduction to avoidance routing
The Problem Formulation
  The Adversary Model
  Our Assumptions
  The Bounded Condition
  The Safe Path Condition
Multi-Path Based Avoidance Routing (MPAR)
Performance Evaluation
Conclusions

## Slide 7: The Adversary Model
Adversaries are assumed to have unbounded computational power
  A nation may spend a large amount of computing and human resources in a critical environment, e.g., a battlefield
  Traffic analysis is also of concern
Perfect secrecy and polynomial secrecy
  An encryption scheme with perfect secrecy is secure against adversaries with unbounded computational power
    e.g., the one-time pad, i.e., , where and the key can be used only once
  An encryption scheme with polynomial secrecy is secure against adversaries with polynomial amount of compt. power

## Slide 8: The Adversary Model
Attack 1: eavesdropping
  Polynomial secure encryptions are assumed not to be safe
Attack 2: denying message forwarding
  Intermediate nodes can compromise encrypted data and drop packets
The protocol design goals
  A routing path should never contain adversaries
  A routing path should avoid insecure area

## Slide 9: Our Assumptions
Known adversaries’ location
  Each node knows binary information (if malicious nodes are in its transmission range
Collusion attacks
  The adversaries in a connected component can collude
 | Unknown location | Known location
Independent | likely | unlikely
Collusions | unlikely | likely
Table. Realistic scenario
Fig. Connected components of adversaries

## Slide 10: The Performance Bound
Condition 1: The bounded condition
  A set of adversaries does not consist of a graph cut
  This tells us the upper bound of performance
    No routing protocol can securely deliver messages if there exists a graph cut by a set of adversaries
Fig. 1. A graph cut
Fig. 2. A path w/o adversaries
An ideal protocol w/ a perfectly secure encryption protects messages from eavesdropping

## Slide 11: The Existing Solutions
The existing solutions
  Avoidance routing for the internet
  Distance vector-based or beacon vector-based routing
Condition 2: The safe path condition
  There exists a path s.t. no node on the path has any adversary in its neighbors
Fig. 1. A safe path
All the existing solutions are single-path-based, and thus the safe path condition dominates the upper bound

## Slide 12: The Gap
There is a big gap between the bounded condition and the safe path condition
  Any single-path routing with a polynomial encryption scheme requires the safe path condition
There is no graph cut by a set of adversaries
There is no safe path between and
Fig. A graph with no safe path

## Slide 13: 3. Multi-Path Avoidance Routing (MPAR)
Introduction to avoidance routing
The Problem Formulation
Multi-Path Based Avoidance Routing (MPAR)
  The Overview of MPAR and Definition
  A Framework
  The K-Path Discovery protocol
  The Performance and Security Properties
Performance Evaluation
Conclusions

## Slide 14: The Overview of MPAR
We propose multi-path avoidance routing (MPAR)
  An on-demand protocol
The XOR coding
  No common secret
  Perfect secrecy by a one-time pad like scheme
Multi-path
  An adversary cannot recover a message unless she wiretaps all the paths
Fig. The idea of MPAR

## Slide 15: Adversary Disjoint Paths
Definition: adversary disjoint paths
  A set of paths that have no common adversary is said to be adversary disjoint paths
Fig. 1. Adversary disjoint paths
Fig. 2. Not adversary disjoint

## Slide 16: Adversary disjoint paths with collusion attacks
Adversary disjoint paths with collusion attacks
Fig. 1. Not adversary disjoint
Fig. 2. Adversary disjoint

## Slide 17: The Performance Bound of MPAR
Condition 3 : the MPAR condition
  There exists at least one set of adversary disjoint paths between the source and destination
  MPAR requires condition 2 or 3
All the network graphs
Condition 1
The bounded condition
Condition 3
Adversary disjoint paths exist
Condition 2
A safe path exists

## Slide 18: The MPAR Framework
MPAR ()
Route_Discovery()
if a safe path is found
sends via
else if there is adversary disjoint paths
computes () by
let
sends via
else
routing fails
# Condition 2 is met
# The single-path mode
# Condition 3 is met
# The k-path mode
# Neither Condition 2 nor 3 are met

## Slide 19: The Route Discovery
The k-path route discovery : ()
  It consists of the route request and reply phases
    and , where is path ID
  A set of adversary's IDs are kept in RREQ and RREP
  A path is set up in the reverse order
The path ID
The source ID
The destination ID
The predecessor ID
The descendant ID
Table. An entry of routing table
Fig. The route discovery

## Slide 20: The Route Discovery (Cont.)
Flooding is repeated until a safe path or a set of adversary disjoint paths are found, or the number of flooding exceeds
Fig 1. The first RREQ
Fig 2. The second RREQ
RREP:
RREP:
RREP:
RREP:

## Slide 21: Limitations
MPAR does not work if an adversary is located in proximity of the source and destination
  Probably only the ideal routing protocol with a perfectly secure encryption scheme can handle this case
  Or cooperative jamming is required
We have not optimized the k-path discovery yet
  The optimal set is
  The worst case is
Fig. Three paths

## Slide 22: The Key Properties
The cost of the k-path discovery
  MPAR introduces additional flooding cost only when a safe path is not found
The cost of the message transmission cost
  MPAR switches to the k-path routing mode, which requires k number of message transmissions, only when a safe path is not found

## Slide 23: The Security Property
The security property of MPAR
  MPAR achieves the perfect secrecy unless a set of adversaries obtain all the XORed messages
The proof is by Shannon’s Theorem
  The encryption scheme over the message space is perfectly secure for which is perfectly secure if and only if
    Every is chosen with equal probability by a random generator
    For every and every , there exists s.t. the encryption scheme outputs

## Slide 24: The Security Property (Cont.)
The proof overview
  Assume that are sent out, and MPAR achieves the perfect secrecy as long as a set of adversaries do not have for some
  works as a cipher
  The missing part works as a key
  are randomly generated, and thus is random
  =>
  For every , there exits a unique s.t.

## Slide 25: 4. Performance Evaluation
Introduction to avoidance routing
The Problem Formulation
Multi-Path Based Avoidance Routing (MPAR)
Performance Evaluation
  Simulation Configurations
  Simulation Results
Conclusions

## Slide 26: Simulation Configurations
We compared MPAR with two protocols
  The ideal protocol w/ a perfectly secure encryption scheme (The upper bound of avoidance routing performance)
  Greedy-AA (a distance vector-based protocol)
Parameters | Values
Simulation area | 800 by 800
Communication range | 100
Number of nodes | 100 to 400 (4.9 ~ 19.6 neighbors / node)
Percentage of adversaries | 0 to 10 % (Adversaries are randomly deployed)
Table. Simulation parameters

## Slide 27: Independent Adversaries

## Slide 28: Collusion Attacks

## Slide 29: 5. Conclusions
In this work,
  We study avoidance routing in ad hoc networks
  We derive the bounded condition and the safe path condition
  We propose multi-path avoidance routing (MPAR)
    The XOR cording and k-path route discovery
    The perfect secrecy
    A weaker condition than that required by the existing protocols
  We demonstrate the performance of the proposed scheme by simulations
Future works
  The optimization of a set of adversary disjoint paths and the cost of finding k-path