## Slide 1: Energy-Aware Scheduling for Aperiodic Tasks on Multi-core Processors
Dawei Li and Jie Wu
Department of Computer and Information Sciences
Temple University, Philadelphia, USA
The 43rd International Conference on Parallel Processing

## Slide 2: Agenda
Introduction
Motivational Example
System Model and Problem Definition
Preliminaries
Solution: subinterval-based scheduling
  Scheduling by the Evenly Allocating Method
  Scheduling by the DER-based Allocating Method
Simulation
Conclusion

## Slide 3: Agenda
Introduction
Motivational Example
System Model and Problem Definition
Preliminaries
Solution: subinterval-based scheduling
  Scheduling by the Evenly Allocating Method
  Scheduling by the DER-based Allocating Method
Simulation
Conclusion

## Slide 4: Introduction
Energy consumption of computer systems has become a critical issue.
For simple task models, namely, framed-based tasks, periodic tasks, and sporadic tasks, intensive works have been done for energy-aware scheduling on both uniprocessors and multiprocessors.
However, energy-aware scheduling for general aperiodic tasks on multiprocessors lacks extensive research endeavors.

## Slide 5: Introduction
Energy-aware scheduling for general aperiodic tasks on uniprocessors.
YDS algorithm: finds the subinterval [t1, t2] with the greatest intensity.
Simple, fast, optimal.

## Slide 6: Introduction
Energy-aware scheduling for general aperiodic tasks on multi-core processors.
Existing works:
  Problem is still polynomial time solvable.
  However, algorithms require high complexity.
    E.g.
    relies on repeated maximum flow computations.
    where n is the number of tasks, and f(n) is the complexity of finding a maximum flow in a graph with O(n) vertices.

## Slide 7: Introduction
We consider energy-aware scheduling for general aperiodic tasks on multi-core processors.
Contributions:
  Show that the energy-aware scheduling problem with the consideration of static powers is still polynomial time solvable, however, also with high complexity.
  Instead of seeking optimal solutions with high complexity, we propose a lightweight algorithm suitable for real-time systems to solve the problem efficiently with good performances.
  We demonstrate the practical usage of the proposed algorithms by various simulations.

## Slide 8: Agenda
Introduction
Motivational Example
System Model and Problem Definition
Preliminaries
Solution: subinterval-based scheduling
  Scheduling by the Evenly Allocating Method
  Scheduling by the DER-based Allocating Method
Simulation
Conclusion

## Slide 9: Motivational Example
Denote the time that each task occupies a core during interval [4, 8], as x1; x2; x3, respectively. Also, denote the total time that task 1 occupies a core during intervals [0, 4] and [8, 12] as y1, and the total time that task 2 occupies a core during the intervals [2, 4] and [8, 10] as y2.

## Slide 10: Agenda
Introduction
Motivational Example
System Model and Problem Definition
Preliminaries
Solution: subinterval-based scheduling
  Scheduling by the Evenly Allocating Method
  Scheduling by the DER-based Allocating Method
Simulation
Conclusion

## Slide 11: System Model and Problem Definition
We consider scheduling a set of independent aperiodic tasks
Each task
Processor power model
Problem formulation:

## Slide 12: Agenda
Introduction
Motivational Example
System Model and Problem Definition
Preliminaries
Solution: subinterval-based scheduling
  Scheduling by the Evenly Allocating Method
  Scheduling by the DER-based Allocating Method
Simulation
Conclusion

## Slide 13: Preliminaries
Characteristics of an Optimal Solution
  Observation 1: in an optimal solution, no matter how many segments a task’s execution consists of, the execution frequencies for this task during all its intervals should be equal, i.e.
  Applying the Lagrange Multiplier Method:

## Slide 14: Preliminaries
Problem Reformulation
  We sort all Ri and Di values in ascending order, and relabel the distinct values as t1, t2,…, tN , where N <= 2n is the total number of distinct Ri and Di values.
  Denote x_{i,j} as the execution time of task i during the jth subinterval.

## Slide 15: Preliminaries
Problem Reformulation
  Theorem 1: The energy minimal scheduling of aperiodic tasks on multi-core processors with static power consumptions and migrations allowed is polynomial time solvable.
  Proof from two aspects, the mathematical problem is polynomial time solvable; and based on this, tasks are schedulable.

## Slide 16: Preliminaries
Problem Reformulation
  Observation 2: during a subinterval [t_j, t_{j+1}], if it is a lightly overlapped subinterval, the overlapping tasks during this subinterval are valid to occupy a processing core for the whole subinterval.
  The key problem lies in how to allocate available execution times to overlapping tasks during a heavily overlapped subinterval.

## Slide 17: Agenda
Introduction
Motivational Example
System Model and Problem Definition
Preliminaries
Solution: Subinterval-Based Scheduling
  Scheduling by the Evenly Allocating Method
  Scheduling by the DER-based Allocating Method
Simulation
Conclusion

## Slide 18: Solution: Subinterval-Based Scheduling
An Ideal Case, where the number of processors is unlimited.
Scheduling by the Evenly Allocating Method
  the execution requirement completed in interval [tj, tj+1] is equal to the ideal optimal case.
  The intermediate scheduling: allocate each task i an available execution time of during the interval [tj, tj+1].

## Slide 19
Consider the tasks one by one, and fill in the cores one by one.

## Slide 20
4 core

## Slide 21: Solution: Subinterval-Based Scheduling
Scheduling by the Evenly Allocating Method
    The final scheduling: After determining the execution time in each subinterval, we can calculate the overall available execution time.
    A refined scheduling can be constructed, which can further reduce energy consumption. A_i^{F_1} is the total available execution time.
    Optimal frequency setting for each task:

## Slide 22: Solution: Subinterval-Based Scheduling
Scheduling by the DER-based Allocating Method
  DER: Desired Execution Requirement
  The intermediate scheduling: Allocate available execution time according to task’s desired execution requirement (referring to the ideal optimal case) during each subinterval.

## Slide 24: Solution: Subinterval-Based Scheduling
Scheduling by the DER-based Allocating Method
  Final Scheduling of the DER-based Allocating Method: Refine the scheduling to further reduce energy consumption.

## Slide 25: Agenda
Introduction
Motivational Example
System Model and Problem Definition
Preliminaries
Solution: Subinterval-Based Scheduling
  Scheduling by the Evenly Allocating Method
  Scheduling by the DER-based Allocating Method
Simulations
Conclusion

## Slide 26: Simulations
Influence of Platform’s Characteristics

## Slide 27: Simulations
Influence of Platform’s Characteristics

## Slide 28: Simulations
Influence of Tasks’ Characteristics

## Slide 29: Simulations
Influence of Tasks’ Characteristics

## Slide 30: Agenda
Introduction
Motivational Example
System Model and Problem Definition
Preliminaries
Solution: Subinterval-Based Scheduling
  Scheduling by the Evenly Allocating Method
  Scheduling by the DER-based Allocating Method
Simulation
Conclusion

## Slide 31: Conclusion
The energy-aware scheduling for general aperiodic tasks on multi-core processors is addressed.
We formulate the problem on multi-core processors in a formal way, which shows that it is polynomial time solvable.
Instead of seeking optimal solutions with high complexity, we design a lightweight algorithm to solve the problem efficiently with good performances.
We demonstrate the practical usage of the proposed algorithms by various simulations

## Slide 32
Additional questions can be sent to dawei.li@temple.edu
The End,
Thank you!