## Slide 1: Social Feature-based Multi-path Routing in Delay Tolerant Networks
Jie Wu and Yunsheng Wang
Department of Computer and Information Sciences
Temple University

## Slide 2: Delay Tolerant Networks (DTNs)
Occasionally connected networks
Examples of DTNs
    Deep space communication
    Wildlife monitoring
    Vehicular communication
    Social contact networks
  Efficient routing is still a main challenge!

## Slide 3: Motivation 1
Existing DTN routing:
  contact history
  mobility pattern
Collecting such information is costly
We use internal social feature information for routing without overhead.

## Slide 4: Motivation 2
Increase delivery rate: multiple copy
  Flooding (O(N))
  Delegation forwarding (O(√N))
It is hard to control the efficiency
Our approach:
  Feature-based (race, gender, language, …)
  logN *copies in node-disjoint paths
  (N * is a group: a node in the hypercube)

## Slide 5: Social Feature
Mobile & unstructured contact space (M-space)
Static & structured feature space (F-space)
Each individual with a social feature profile {F1, F2,…}
Individuals with the same features mapped to a group

## Slide 6: Example
      People come in contact with each other more frequently if they have more social features in common (P1>P3, P2>P3)
P1
P2
P3

## Slide 7: Feature Extraction
Extract m most important features
Extract most informative subset (MIS) with m(from m′) key features based on entropy
  E(Fj) : entropy of Fj
  p: probability mass function of Fj

## Slide 8: The entropy of each social feature (Infocom 2006 trace)
Social Feature | Entropy
Affiliation | 4.64
City | 4.45
Nationality | 4.11
Language | 4.11
Country | 3.59
Position | 1.37

## Slide 9: A 3-dimensional (3-D) hypercube
City: New York(0), London(1), Paris (2), Shanghai (3)
Position: professor (0), researcher (1), student (2)
Gender: male (0), female (1)
Dimension 1: city
Dimension 2: position
Dimension 3: gender
Example: “311” : a female researcher lives in Shanghai

## Slide 10: Property of Hypercube
Efficient copy management in an m-d binary cube (S and D differ in k features)
m node-disjoint paths from S to D
  k shortest paths of length k
  m−k non-shortest paths of length k+2.

## Slide 11: Hypercube Routing
The relative address of the current group and destination group (a small string in the header)
  calculated through XOR on S and D
  sent, along with the packet, to the next node
Any node in the group can forward to any node in the adjacent group
Special treatment is needed at the destination group

## Slide 12: Coordinate sequence
  Path 1: <1, 2, 3> (red directed line)
  Path 2: <2, 3, 1> (blue directed line)
  Path 3: <3, 1, 2> (green directed line)
Node-disjointness

## Slide 13: Example: Node-Disjoint-based Routing
S = G0 and D = G6

## Slide 14: Example: Node-Disjoint-based Routing
2 shortest node-disjoint paths:
  <1, 2>: red directed line
  <2, 1>: blue directed line
1 non-shortest node-disjoint path:
  <3, 2, 1, 3>: dashed directed line

## Slide 15: Shortcuts
Feature matching shortcut can resolve the feature distance more than one at a time.
Shortcut reduces the number of forwardings while ensuring the path disjointness property.

## Slide 16
An example of the composite path from 0000 to 1111.
Composite path: all possible paths from one node to another in a certain dimension sequence, including the direct path (solid directed line) and all possible shortcut paths (dashed directed lines).

## Slide 17: Comparison of contact frequency with different feature distance in the Infocom 2006 trace
Direct frequency: Pi..j
Shortcut frequency: Pij
Composite frequency: P’i..j

## Slide 18: Two Observations
Observation 1: the shortcut frequency (Diagonal line) (P3)
  smaller than each side (P3 < P1 or P2)
  Larger than the product of two sides (P3 > P1 * P2)
Observation 2: the composite frequency (Diagonal line) (P’1..2 = P3 + P1 * P2)
  smaller than each side (P’1..2 < P1 or P2)
  Larger than the product of two sides (P’1..2 > P1 * P2)

## Slide 19: Simulation
Synthetic trace
  A node A has m contact frequencies, p1, p2, . . . , pm, with its m neighbors in the m-D F-space.
  128 individuals
  m is 4, 5, 7, 8, and 11.
Real trace
  Infocom 2006 trace.
  61 participants
  6 social features, m is 3, 4, 5, and 6.

## Slide 20: 7 routing schemes comparison
Node-disjoint-based with wait-at-destination (ND-W)
  Waiting for the destination after the packet enters the destination group
Node-disjoint-based with spray-at-destination (ND-S)
  Spraying N/(2M) copies into the destination group after the packet enters the group
Delegation-based with wait (D-W)
Delegation-based with spray (D-S)
  Delegation-based: The copies of a packet is only forwarded to the individual with a smallest feature distance to the destination it has met so far
Note: spray is needed at the destination group to increase the chances to meet the actual destination!

## Slide 21: 7 routing schemes comparison-cont’d
Source spray-and-wait (S-S&W)
  The source forwards copies to the first m distinct nodes it encounters. If the destination is not found, the copy carriers wait for the destination.
Binary spray-and-wait (B-S&W)
  Any node with copies will forward half of the copies to the encountered node with no copy.
Binary spray-and-focus (B-S&F)
  The copy carriers forward the copy to the encountered node with a smaller feature distance to the destination.

## Slide 22: Varying node density – delivery rate
Synthetic trace
Real trace

## Slide 23: Varying node density – latency
Synthetic trace
Real trace

## Slide 24: Varying node density – # of forwardings
Synthetic trace
Real trace

## Slide 25: Conclusions
Unstructured mobile contact space (M-space)
Static structured social feature space (F-space)
Extract the most informative features to create a hypercube
Multi-path routing:
  Feature-based, efficient copy management, and node-disjoint-based
Future work
  Binary cubes to general cubes
  Network coding, e.g., Fountain code

## Slide 26
Questions ?

## Slide 27: shortcut
Comparing shortcut and non-shortcut with 100 packets in the real trace

## Slide 28: Non-shortest path