## Slide 1
Dynamic Adaptation of In-Band Network Monitoring via Meta Learning Mingyuan Zang∗, Eder Ollora Zaballa‡, Lars Dittmann‡, Jie Wu∗†
∗ China Telecom Cloud Computing Research Institute,
‡Technical University of Denmark, † Temple University
IEEE 50th Conference on Local Computer Networks (LCN)

## Slide 2: Internet of Things (IoT) Network
ML-based Analysis
Diverse use cases
Heterogeneous Access
Internet
5G/6G’s extremely low latency requirements + emerging attack variants in IoT
→ Fast spreading threats with changing patterns
IEEE 50th Conference on Local Computer Networks (LCN)

## Slide 3: Internet of Things (IoT) Network
3
Programmable data planes enable flexible in-network traffic processing
Diverse use cases
Heterogeneous Access
Internet
IEEE 50th Conference on Local Computer Networks (LCN)

## Slide 4: Dynamic Traffic Pattern
In-Band Feature Collection
Collected Features:
Number of UDP packets
Number of unique port pairs
Max/min packet length
…
Port Scan attack as an example:
A UDP packet sent to all ports and response from the target port
reflected by port, length distribution in packets
IEEE 50th Conference on Local Computer Networks (LCN)
UDP + Port 53
UDP + Port 53 Data
UDP + Port 54
…

## Slide 5: Dynamic Traffic Pattern
In-Band Feature Collection
Collected Features:
Number of TCP packets
Number of TCP SYN flags
Inter-Arrival Time (IAT)
…
DDoS LOIT as an example:
Halfway handshakes triggered by numerous SYN
Reflected by the number, rate and TCP flags of packets within a time window
IEEE 50th Conference on Local Computer Networks (LCN)
SYN
SYN
SYN ACK
SYN ACK
…

## Slide 6: Dynamic Feature Importance
Dataset: MQTT2020
Dataset: CICIDS2017
IEEE 50th Conference on Local Computer Networks (LCN)
Distribution of Feature Importance
Same group of features shows different levels of importance in attack identification
e.g. Inter-arrival time

## Slide 7
How to adaptively collect the new feature sets?

## Slide 8: Programmable Data Plane
IEEE 50th Conference on Local Computer Networks (LCN)
- Apply P4 for in-band feature collection
- ML algorithm for accurate & generalizable detection
Programmable data plane with P4 language
Protocol-Independent architecture
Custom packet header & processing
More flexibility on the data plane
Design Target
Eth
Custom hdr
Data
IP
Control plane
Incoming traffic
Update
Data plane
Forward
traffic
Feature Parse
Feature Analysis

## Slide 9
How to adaptively learn from new traffic patterns?

## Slide 10: Proposed Design – Meta Learning
Support Set
,
Target Set
,
Model
Support Set
Loss
Optimizer
Target Set
Inner Loop
Outer Loop
Weight Update
Weight Update
IEEE 50th Conference on Local Computer Networks (LCN)
Rapid adaptation to new scenarios with minimal data learned
Our work: Model-Agnostic Meta-Learning (MAML)
Optimization-based meta-learning
Inner loop (quick adaptation) + outer loop (stable convergence)
Stronger generalization
“Learning to learn”

## Slide 11: Proposed Design – Framework
Cloud/Server
Traffic
Data Plane
Controller
1
Switch
Header fields are parsed and protocol information is extracted
IEEE 50th Conference on Local Computer Networks (LCN)
Step 1 Packet Parsing
Eth
UDP
Data
IP

## Slide 12: Proposed Design – Framework
Cloud/Server
Traffic
...
Feature Extraction
3
Data Plane
Controller
1
2
Switch
Feature
Selection
IEEE 50th Conference on Local Computer Networks (LCN)
Stateful features are computed by hashing and updating counter registers
Step 2 & 3 Statistic Extraction

## Slide 13: Proposed Design – Framework
Cloud/Server
Traffic
...
UDP ... Payload
Feature Extraction
3
Report Encapsulation
Data Plane
Controller
1
4
2
Switch
Feature
Selection
IEEE 50th Conference on Local Computer Networks (LCN)
When a packet arrives at the ingress port, a timestamp is recorded
Once the timestamp exceeds time window T, collected features {f1,..., fn} are read
Features are encapsulated in UDP report
Step 4 Report Encapsulation

## Slide 14: Proposed Design – Framework
Cloud/Server
Traffic
...
UDP ... Payload
Feature Extraction
3
Report Encapsulation
Feature Alignment
Data Plane
Controller
1
4
5
2
Switch
Feature
Selection
IEEE 50th Conference on Local Computer Networks (LCN)
Feature alignment is performed to adapt to new feature sets
Step 5 Feature Alignment

## Slide 15: Proposed Design – Framework
Cloud/Server
Traffic
...
UDP ... Payload
Feature Extraction
3
Report Encapsulation
Feature Alignment
Data Plane
Controller
1
4
5
2
Switch
Few-shot Classification
6
Feature
Selection
IEEE 50th Conference on Local Computer Networks (LCN)
Features are parsed and labeled by a pre-trained meta-learning model
The model is trained offline and then loaded for real-time inference on a small number of examples
Step 6 Few-Shot Classification

## Slide 16: Evaluation Results
Public Dataset: public dataset CICIDS 2017, IoT Sentinel, MQTT2020
ML Baseline: Autoencoder, PotoNet, OnlineML
Prototype: BMv2 programmable switch + topology emulated in Mininet
Performance
>70% accuracy, better trade-off between accuracy/inference time, 1.5× faster latency
IEEE 50th Conference on Local Computer Networks (LCN)

## Slide 17: Evaluation Results
IEEE 50th Conference on Local Computer Networks (LCN)
Performance
outperform baseline algorithms by 8%-17% higher accuracy across few-shot samples
Dataset: CICIDS2017
Dataset: IoTSentinel
Dataset: MQTT2020

## Slide 18: Conclusion
We present a framework to adaptively collect the new feature sets and promptly learn from them:
Accurate ML-based traffic analysis with reconfigurable feature parsing
Generalizable performance with reasonable learning time
- Lower manual recompilation overhead
Further work:
Scalable deployment scheme on hardware
IEEE 50th Conference on Local Computer Networks (LCN)
Thanks! Questions?

## Slide 19: Proposed Design – Framework
Cloud/Server
Traffic
...
UDP ... Payload
Feature Extraction
3
Report Encapsulation
Feature Alignment
Data Plane
Controller
1
4
5
2
Switch
Few-shot Classification
6
Feature
Selection
Data Plane
...
UDP
...
UDP
Data Plane
Header fields are parsed and protocol information is extracted
IEEE 50th Conference on Local Computer Networks (LCN)
Step 1 Packet Parsing
Eth
UDP
Data
IP