## Slide 1: Robust Wireless Delivery of Scalable Videos using Inter-layer Network Coding
Pouya Ostovari and Jie Wu
Computer and Information Sciences
Temple University
Center for Networked Computing
http://www.cnc.temple.edu

## Slide 2: Agenda
Introduction
  Multi-layer video coding
  Robustness multi-layer video streaming
Evaluations
Conclusions
Notes: First I will provide an introduction and motivation for our work
Then, I will talk about the benefits on network coding in robustness and throughput enhancement,
and I will talk about our partial results and future work.
At the end, I will conclude my talk

## Slide 3: Introduction
Advances in technology
  Smartphones and tablets
  Internet is accessible everywhere
  Video streaming is used widely and frequently
Video streaming is a dominant form of traffic on the Internet
  YouTube and Netflix:
    Produce 20-30% of the web traffic on the Internet
Notes: In recent days, we are witnessing a fast development in the hardware technologies of mobile devices
such as tablets and smartphones
As a result of these advances, the mobile devices are becoming very popular
Using wireless connections is more convenient than the wired connections.
Moreover, they can solve the last mile problem

## Slide 4: Introduction
Scalable video coding
  Delivering video stream using different resolutions to satisfy different client needs/constraints
Multi-Layer Coding
  Base layer
  Enhancement layers
A challenge in multicasting
  Different link conditions
  Loss rate, bandwidth
Notes: Scalable videos are useful in delivering video stream with different resolutions to users with different needs
There are two forms of scalable videos
Multi-layer and multi-description coding

## Slide 5: Multi-Layer Video Streaming
H.264/SVC coded
  Temporal layers
  Quality layers
  Spatio layers
Temporal
Quality layer 1
Unequal error protection
  Grouping the packets of multiple GOP together
  Providing different levels of protection for different groups
    Intra-layer network coding
  Different heuristics are proposed
    They focus on measuring the effect of each layer on the video quality
Quality layer 2
Notes: H.264/MPEG-4 or advanced video coding (AVC) is a video compression format
It is one of the most commonly used formats for compression and distribution of video content
H.264/SVC, which is an extension of the H.264/AVC, supports spatial, temporal, and quality scalabilities
GOP is a group of successive pictures within a coded video stream

## Slide 6: Inter-Layer Coding Strategies
Random linear network coding (RLNC)
Packets in lower layers are more important
  Included in more coded layers
  More chance to be decoded
Triangular coding
  Prefix coding
Notes: If a user receives enough coded packets, it can decode and retrive all of the layers
Otherwise, it will not be able to decode any layer.
Because of this problem, a modification on RLNC is prosed, called triangular network coding

## Slide 7: Advantage of Triangular Coding
Coefficients are not shown for simplicity
6 transmissions in round-robin pattern
  Blue cells are received
L1 + L2+ L3
L1 + L2+ L3
L1 + L2+ L3
L1 + L2+ L3
L1 + L2+ L3
L1 + L2+ L3
L1
L2
L3
L1
L2
L3
No coding
Random linear coding
Unable to decode
Unable to decode
L1
L1 + L2
L1 + L2+ L3
L1
L1 + L2
L1 + L2+ L3
Triangular coding
Decodes 2 layers

## Slide 8: Two-Dimensional Inter-Layer NC
Performing inter-layer triangular NC on quality and temporal layers

## Slide 9: Two-Dimensional Inter-Layer NC
Vertical triangular NC
Horizontal triangular NC
Diagonal triangular NC

## Slide 10: Transmissions Distribution
Fixed number of transmissions
Reference table creation
  Considering all the possible distributions
  Checking the possible outcomes
  Calculating the layers that can be decoded
Searching in the reference table to find the best transmission distribution

## Slide 11: Evaluations- Setting
Comparison with Percy method
  Is performed among the spatio layers
Bus video trace
  352×288 pixels, 30 frames
  4 temporal layer
  3 spatio layers
    Layer 1: 176×144
    Layer 2: 320×240
    Layer 3: 352×288

## Slide 12: Evaluations- Setting
Original video
Base spatio layer

## Slide 13: Evaluations

## Slide 14: Evaluations

## Slide 15: Evaluations

## Slide 16: Conclusions
Challenges in multicasting
Dependency in multi-layer videos
Unequal error protection
Two-dimensional triangular network coding
Trace-driven evaluation

## Slide 17
Thank you