## Slide 1: Quantized Conflict Graphs for Wireless Networks Optimization
Yanchao Zhao，Wenzhong Li, Jie Wu & Sanglu lu
@ Nanjing University & Temple University

## Slide 2: Background
Wireless Networks are Ubiquitous
  WiFi
  3G/4G Network
  Wireless Sensor Network
  Wireless Mesh Network
Wireless Medium is shared
  The number of channels is limited
  The bandwidth of channels is limited
  Spatial Reuse is conflict with Coverage range

## Slide 3: Background
Wireless Throughput Optimization
More Users Supported
Better Spectrum Utilization
Larger Bandwidth
How to allocate the communication resources to achieve best services?

## Slide 4: Interference Model for Wireless Network Optimization
Wireless Network Optimization
FDM
Link Scheduling
TDM
Spatial Reuse
Power Control
Channel Assignment / Spectrum Allocation
Routing
Bit-Rate Control
Cross-layer Optimization
Interference Model
Association Control
Conflict Relation
Amount of Interference
Relation between Interference and Capacity

## Slide 5: Why do we need a new model
Physical Interference Model (SINR Model)
Protocol Interference Model (Conflict Graph)
Accurate
Classic Graph Algorithm
Accumulative Interference
Exhausting Measurement
Non-convex
Coarse-grained
A Quantized Conflict Graph Model
Partial Measurement
Finer-grained
Classic Graph Algorithm

## Slide 6: Motivation Example
GH
AB
CD
EF
Total Interference : 0.94
0.16
0.33
0.45
Traditional conflict graph
Notes: ----- 会议笔记(15/4/20 14:56) -----
加值

## Slide 7: Motivation Example
Total Interference
: 0.81
0.16
0.65

## Slide 8: QCG Definition
Quantized Conflict Graph
Pros
Do not require an accurate RSS to get the same allocation Results
Rough RSS representation could increase the prediction accuracy
We apply a Step function
to map the RSS to the M-level weights in the graph

## Slide 9: Framework
Quantized Conflict Graph
How to generate QCG Efficiently and Accurately?
How to utilize the QCG to solve the Wireless Optimization Problem in a low computational cost?

## Slide 10: Properties of QCG
Exhaustive signal measurements at outdoor/indoor WiFi networks
  Transformed into Quantized RSS Matrix
Dataset | In/out | Area (km2) | #of APs | Avg # of APs heard per location | # of measured locations
MetroFi | Outdoor | 7 | 70 | 2.3 | 30,991
SWIM Platform | Indoor | <1 | 10 | 5 | 40

## Slide 11: Properties of QCG
Explore the low-rank Property
Real RSS Matrix has low rank Property

## Slide 12: Properties of QCG
Explore the similarity between rows
Similarity between rows of RSS matrix is high

## Slide 13: Efficient QCG Estimation
Our approach: measure a few, predict many
Measurement Cost
Model Accuracy
Exhaustive measurements
Non-measurement methods
Our Goal

## Slide 14: Efficient QCG Estimation
Basic Idea
Quantized Conflict Graph
Utilize the Properties of Quantized RSS Matrix
Treat Quantized RSS prediction as a Matrix Completion Problem

## Slide 15: Efficient QCG Estimation
Low-rank Approximation
Measurement Constraint
Rank Constraint
Propagation Constraint
Miss the similarity property between rows

## Slide 16: Efficient QCG Estimation
Similarity
  We applied the idea of k-nearest neighbor here
Good to deal with the Matrix with small portion of Missing Elements

## Slide 17: Efficient QCG Estimation
Comprehensive
  Trivial to combine the similarity and low-rank approximation together and improve the accuracy
Use the low-rank approximation to compute a matrix X
Compute the Similarity between rows in X
Apply the linear regression for k-largest similar rows to compute weights
Compute un-known entries with the weights computed in last step

## Slide 18: QCG-based Optimization
Interference Minimization
Definition
K channels, N nodes(links)
Minimize the total network interference
Max K-cut Problem
Scheduling
Definition
K channels, N nodes(links)
Minimize the total network interference
Max Weighted Independent Set

## Slide 19: Evaluation
Prediction Accuracy
Comprehensive Method perform best with the others mutually complementary
Increase the number of levels larger than 10 only slightly improve the accuracy
Notes: ----- 会议笔记(15/4/20 14:56) -----
Motivation 精炼
为什么要weight
logo加南大
logo加页码
配色

## Slide 20: Evaluation
Wireless Network Optimization

## Slide 21
Questions?
Thanks