## Slide 1: Throughput and Fairness-Aware Dynamic Network Coding in Wireless Communication Networks
Pouya Ostovari
Jie Wu

## Slide 2: Agenda
Introduction
Motivation and setting
Proposed methods
  Dynamic network coding
  Fair dynamic network coding
Simulation results
Conclusion

## Slide 3: Network Coding in Wired Networks
Bottleneck problem
Without coding
With coding
Notes: Network coding first introduced for wired networks and showed that it can solve the bottleneck problem.

## Slide 4: Network Coding in Wireless Networks
No coding
  4 transmissions
Coding
  3 transmissions
Inter-flow coding
  Increases the throughput
Notes: The wireless nature of the medium makes network coding more attractive in wireless networks.

## Slide 5: Network Coding in Wireless Networks
Intra-flow coding
  Reliability
Notes: The reliability of the link is 2/3. The source wants to transmit 2 packets to the destination node. With coding, the source on average transmits 3 coded packets and the destination receives 2 coded packets, which are sufficient for decoding. However, without coding, feedback mechanism is required to show the lost packet.

## Slide 6: Setting
One source
  Broadcasts a set of packets
Multiple destinations
  Independent erasure channels
Equal size time slots
  One packet transmission per time slot
Objective
  Throughput

## Slide 7: Introduction (Segment Coding)
Segment coding
Dynamic coding

## Slide 8: Introduction
Seen packet (Sundararajan’08)
  A node has seen a packet P if it can generate a linear combination of the form P + Q, using the received coded packets in its buffer
  1
  1
  Seen packets can be removed from the sender’s buffer

## Slide 9: Introduction
ARQ with network coding (ANC)

## Slide 10: Idea
Behind and leader nodes
Code packets in the range of the first unseen packets by the leader and behind nodes

## Slide 11: Multiple Behind and Leader Nodes
2 methods to deal with multiple behind and leader nodes

## Slide 12: Dynamic NC without Overhearing
All leaders need to transmit a feedback
  A receiver that missed the last transmission cannot be a leader node
  If the index of the first unseen packet is equal to the largest index included in the received coded packet, then the node is a leader node
Behind nodes
  If all the behind nodes receive the current transmissions, they do not send any feedback messages

## Slide 13: Dynamic NC with Overhearing
Two feedbacks per time slot
Just one leader and one behind node send feedback
  Set a back-off time based on the erasure rate of the nodes
  The receivers listen to the channel
  Leader node finishes its back-off time
    Send feedback if has not overheard feedback from the other leaders

## Slide 14: Dynamic NC with Overhearing
Two feedbacks per time slot
Just one leader and one behind node send feedback
  The behind nodes that have received the last transmissions do not need to transmit a feedback
  Only one of the nodes that was a behind node in the previous slot, and missed the current transmission should send a feedback

## Slide 15: Throughput
In ANC each transmission has innovative information for all of the nodes
  Achieves the maximum throughput
  Proof
The same approach can be used to prove that the DNC is throughput optimal

## Slide 16: Fair Dynamic NC
Unfairness of ANC and DNC
  The nodes with low error rates receive more coded packets than the other nodes, and become the leaders
  The nodes with higher error rates might not be able to decode the packet for a long time

## Slide 17: Fair Dynamic NC
A trade-off between fairness and throughput
  w : fairness factor
  L : number of leaders
  m : number of users
If x>0, the sender adds a new packet to the coded packet

## Slide 18: Simulations (Definitions)
Decoding delay unfairness
Decoding delay fairness
Decoding unfairnes

## Slide 19: Simulations
ANC: ARQ with NC
DNC: Dynamic network coding without overhearing
DNC-OH: Dynamic network coding with overhearing

## Slide 20: Simulations (Decoding Fairness)
ANC: ARQ with NC
FDNC: Fain dynamic network coding
MW: Moving window

## Slide 21: Simulations (Delay Fairness)

## Slide 22: Simulations (Throughput)

## Slide 23: Simulations (Decodable Packets)

## Slide 24: Summary
Dynamic coding increases the throughput of network coding
  Too many feedback messages
We propose the DNC and DNC-OH methods to reduce the number of feedbacks
We propose the FDNC method to provide decoding and decoding delay fairness

## Slide 25
Questions