## Slide 1: Node-based Scheduling with Provable Evacuation Time
Bo Ji
Dept. of Computer & Information Sciences
Temple University
E-mail: boji@temple.edu
Joint work with Jie Wu@Temple
CISS 2015
Baltimore, Maryland
March 18th, 2015

## Slide 2
Link Scheduling for
Minimum Evacuation Time
2
Evacuation time: time needed for draining all the existing packets
  A critical metric in settings without future arrivals
    Goal: minimize the evacuation time
  In settings with arrivals, a good measure of short-term throughput & closely related to the delay performance
Multigraph Edge Coloring Problem
multi-edge = packet
color = matching
Multihop wireless networks
Unit link
capacities
Single-hop
traffic flows
One-hop interference model:
feasible schedule = matching
Ex.: Bluetooth, FH-CDMA, etc.
Notes: Evacuation time is a critical metric in settings without arrivals.
In settings with arrivals, it is a measure of short-term throughput, and is closely related to the delay performance

## Slide 3
Multigraph Edge Coloring Problem
3
The problem is generally NP-hard [Holyer’81]
Approximations
  Shannon’s theorem [Shanon’49], Vizing’s theorem [Vizing’64], …
  Any constant-factor approximation ratio better than 4/3 is NP-hard [Holyer’81]
  If a small additive term is allowed, much better approximations (exact or asymptotic) [Sanders & Steurer’08,…]
A survey book on graph edge coloring [Stiebitz et al.’12]
Limitations
  All rely on recoloring-based techniques
  The colors (or schedules) are computed all at once
  The complexity depends on # of multi-edges (or # of packets)
    Could be impractically high
    Unsuitable for link scheduling and packet evacuation
  More limited applications to settings with arrivals

## Slide 4
Online Algorithms
4
Quickly compute one color (or schedule) at a time
  Complexity is only dependent on network size
    Link count and node count
  High complexity is distributed over time
  Desirable for applications such as link scheduling
  Functional even if packet arrivals are considered
Example algorithms
  Maximum Weighted Matching (MWM) algorithm
  MWM-α algorithm
  Greedy Maximal Matching (GMM) algorithm
  Randomized Maximal Matching (RMM) algorithm
Existing online algorithms all have an approximation ratio no better than 2! [Gupta et al.’09]
Edge-based
Load-agnostic

## Slide 5
Node-based Approach
5
Input-queued switches
  Modeled as bipartite graphs
  A class of Lazy Heaviest Port First (LHPF) algorithms [Gupta et al.’09]
    Maximum Vertex-weighted Matching (MVM), also known as Longest Port First algorithm [Mekkittikul & McKeown’98]
    Maximum Node Containing Matching algorithm [Tabatabaee & Tassiulas’09]
  LHPF is both evacuation-time-optimal and throughput-optimal
Multihop wireless networks
  Modeled as general graphs
  Evacuation-time performance is largely unknown
  Our focus: develop and analyze node-based scheduling algorithms with provable evacuation time and lower complexity

## Slide 6
Our Contributions
6
Prove that MVM has an approximation ratio no greater than 3/2 in multihop wireless networks
Propose a new node-based algorithm – Critical Node Matching (CNM) algorithm
  CNM guarantees an approximation ratio no greater than 3/2 as well
  CNM has a lower complexity of O(m √n) than O(m √n logn) of MVM, where m and n are the link count and the node count, respectively
As a byproduct, these algorithms serve as an alternative for achieving Shannon’s bound of 3/2 Δ, where Δ is the maximum node degree

## Slide 7
MVM
7
: # of packets waiting to be transmitted over link l
: set of links incident to node i
: degree of node i
: matching
: set of all the matchings
MVM:
: weight of node i
: weight of matching M
: Maximum Vertex-weighted Matching
The MVM algorithm finds an MVM in each time slot
MVM has a complexity of O(m √n logn)

## Slide 8
MVM - Example
8
3
2
1
1
Ql=2
4
5
3
4
di=2
MVM
MWM, GMM, MWM-α with α>0
4
5
4
wi=2
3
3
2
1
1
wl=2

## Slide 9
Main Result
9
Theorem 1: MVM has an approximation ratio no greater than 3/2.
Proof Sketch:
Minimum evacuation time ≥ maximum node degree = Δ
MVM achieves Shannon’s bound
  Evacuation time of MVM ≤ 3/2 Δ (Proposition 1)
Proposition 1: Suppose the maximum node degree is no smaller than two. Under the MVM algorithm, the maximum node degree decreases by at least two within every three consecutive time-slots.

## Slide 10
Proof Sketch of Proposition 1
10
Proposition 1: Suppose the maximum node degree is no smaller than two. Under the MVM algorithm, the maximum node degree decreases by at least two within every three consecutive time-slots.
Proof Sketch:
If the maximum node degree does not decrease in a time-slot, it will decrease in both of the following two time-slots
  Critical node: Node having a maximum degree
  Lemma 1: If the subgraph induced by all the critical nodes is bipartite, then there exists a matching that matches all the critical nodes [Anstee & Griggs’96]
  Lemma 2: If there exists a matching that matches all the critical nodes, then MVM will match all of them as well
  In both of the following two time-slots, the subgraph included by all the critical nodes is indeed bipartite
Observation: in order to achieve 3/2, it is sufficient to focus on scheduling the critical nodes

## Slide 11
CNM – Lower Complexity MVM
11
Critical Node Matching (CNM) algorithm
  Motivated by the key observation, focus on scheduling the critical nodes
  Assign node weights as follows:
    , if i is a critical node
    , otherwise
    , both B1 and B2 are bounded positive integer
  Find an MVM based on the new weights in each time-slot
An implementation with O(m √n) complexity for bounded integer weights [Huang & Kavitha’12, Pettie’12]
Theorem 2: CNM has an approximation ratio no greater than 3/2.

## Slide 12
CNM - Example
12
3
2
1
1
Ql=2
4
5
3
4
di=2
MVM (also CNM)
4
5
4
wi=2
3
CNM (B1=1, B2=2)
1
2
1
wi=1
1

## Slide 13
Lower Bound of 4/3
13
First time-slot, second, third, and fourth.
MVM & CNM: 4 slots
Optimal: 3 slots

## Slide 14
Throughput & Delay Performance
14
Simulation settings
4X4 grid network
unit link capacity
A flow with arrival rate λ at each link
Observations
MVM & CNM both empirically achieve good throughput performance
MVM empirically achieves best delay performance

## Slide 15
Conclusion
15
Proved that MVM achieves an approximation ratio no greater than 3/2 for the minimum evacuation time problem
By making a key observation that it is sufficient to focus on scheduling the critical nodes for achieving an approximation ratio no greater than 3/2, we proposed a lower-complexity algorithm – CNM – with a same performance guarantee
These algorithms serve as an alternative for achieving Shannon’s bound
Node-based approach is less studied
  Performance limits of the node-based algorithms?
  Conjecture: 4/3 is tight for MVM (and CNM) – much more challenging
  If an additive term is allowed, can we develop node-based algorithms with better approximations (exact or asymptotic)?
  Throughput performance in settings with arrivals?

## Slide 16: Thank You !
Questions?
E-mail: boji@temple.edu