## Slide 1: Deadline-aware Broadcasting in Wireless Networks with Local Network Coding
Pouya Ostovari, Jie Wu, and Abdallah Khreishah
Computer & Information Sciences Department,
Temple University,
USA

## Slide 2: Alice and Bob (No coding)
Alice
R
Bob
X
Y
X
Y
4 transmissions

## Slide 3: Alice and Bob (Coding)
Alice
R
Bob
X
Y
X+Y
3 transmissions

## Slide 4: Deadline-Aware Broadcasting
Z:
  Generation: slot 5
  Deadline: 7
Y:
  Generation: slot 3
  Deadline: 6
X:
  Generation : slot 1
  Deadline: 6
X
Y
1
2
3
4
5
Z

## Slide 5: Deadline-Aware Broadcasting
Z:
  Generation: slot 5
  Deadline: 7
Y:
  Generation: slot 3
  Deadline: 6
X:
  Generation : slot 1
  Deadline: 6
X
Y
1
2
3
4
5
X
X
Y
Y
Time slot 2
Time slot 1
Time slot 3
Time slot 4
Time slot 5
Time slot 6
X
X
Y
Y
Z
Z
Z
Z
Z
Time slot 7
3 transmissions by the relay node
No deadline misses
Without waiting

## Slide 6: Deadline-Aware Broadcasting
Z:
  Generation: slot 5
  Deadline: 7
Y:
  Generation: slot 3
  Deadline: 6
X:
  Generation : slot 1
  Deadline: 6
X
Y
1
2
3
4
5
X
X
Y
Y
Time slot 2
Time slot 1
Time slot 3
Time slot 4
Time slot 5
X+Y+Z
Time slot 6
Z
Z
Z
Z
X+Y+Z
Time slot 7
X
1 transmissions by the relay node
Deadline misses
Waiting time=4

## Slide 7: Deadline-Aware Broadcasting
Z:
  Generation: slot 5
  Deadline: 7
Y:
  Generation: slot 3
  Deadline: 6
X:
  Generation : slot 1
  Deadline: 6
X
Y
1
2
3
4
5
X
X
Y
Y
Time slot 2
Time slot 1
Time slot 3
Time slot 4
Time slot 5
X+Y
X+Y
X+Y
X+Y
Time slot 6
Z
Z
Z
Z
Z
Time slot 7
2 transmissions by the relay node
No deadline misses
X
Waiting time=2

## Slide 8: Setting
All-to-all broadcast
Perfect links
MIMO capability
Two-hop local information
Objective: minimizing the number of transmissions
Constraint: Each packet has a deadline to be received by all nodes.

## Slide 9: High Level Approach
Selecting forwarder nodes
  Any deterministic forwarding method
  Partial Dominant Pruning
Calculating waiting time of each packet at relay nodes
  Velocity based waiting time
  Proportional distribution of waiting time
  Random waiting time

## Slide 10: Partial Dominant Pruning (PDP) (W. Lou and J. Wu, 2002)
The source node selects a subset of its neighbors such that they cover two-hop neighbors of the source.
  Two-hop local information
The source add the forwarder list to the packets.
Each forwarder node performs the same instruction.

## Slide 11: Velocity-Based Waiting Time
1
5
6
7
4
3
2
Time slot=1
Time slot=2
Remaining time of packet i at node j
Deadline of packet i
Current time
Extra time of packet i at node j
Waiting time of packet i at node j
Maximum remaining hop of packet i at node j

## Slide 12: Velocity-Based Waiting Time
1
5
6
7
4
3
2
Time slot=3
Time slot=4
Remaining time of packet i at node j
Deadline of packet i
Current time
Extra time of packet i at node j
Waiting time of packet i at node j
Maximum remaining hop of packet i at node j

## Slide 13: Velocity-Based Waiting Time
1
5
6
7
4
3
2
Time slot=5
Time slot=6
Remaining time of packet i at node j
Deadline of packet i
Current time
Extra time of packet i at node j
Waiting time of packet i at node j
Maximum remaining hop of packet i at node j

## Slide 14: Velocity-Based Waiting Time
1
5
6
7
4
3
2
Remaining time of packet i at node j
Deadline of packet i
Current time
Extra time of packet i at node j
Waiting time of packet i at node j
Maximum remaining hop of packet i at node j

## Slide 15: Velocity-Based Waiting Time
Algorithm

## Slide 16: Coding

## Slide 17: Proportional Distribution of Waiting Time
More Crossing flows more coding chance
Number of flows that pass from node j
Average number of passing flows from children nodes of node j in i-th tree

## Slide 18: PDWT (Initializing Phase)

## Slide 19: PDWT (Running Phase)

## Slide 20: Random Waiting Time
The deadline should be less than to ensure meeting the deadline.
Lower bound:
Upper bound:
The computed waiting time using the proportional method
The extra time of packet i at node j

## Slide 21: Random Waiting Time

## Slide 22: Simulations
VWT: Velocity based Waiting Time
PDWT: Proportional Distribution of Waiting Time
RWT: Random Waiting Time

## Slide 23: Simulations
M=30, G=60
M=30, G=30
VWT: Velocity based Waiting Time
PDWT: Proportional Distribution of Waiting Time
RWT: Random Waiting Time

## Slide 24: Simulations
M=30, G=60
M=30, G=30
VWT: Velocity based Waiting Time
PDWT: Proportional Distribution of Waiting Time
RWT: Random Waiting Time

## Slide 25: Summary
Deterministic forwarding approach
  PDP
Local network coding
Delaying forwarding to increase coding opportunities
  Velocity based waiting time
  Proportional distribution of waiting time
  Random waiting time

## Slide 26
Questions