## Slide 1
ACM SIGKDD 2026 (KDD ’26)
Communication-efficient intelligent sensing under complex weather conditions
Junwei Zhao · Qianchun Luo · Jie Wu*
China Telecom Cloud Computing Research Institute
EDGE
Selective IR
LINK
In-band SEI
CLOUD
Parallel AI
Sensing + Communication
+ Computing, co-designed
Supported by the China Telecom Key Research Project on Intelligent Ubiquitous Cloud Technologies (No. 65996).
Edge–Cloud Collaborative Multimodal
Dehazing for UAV Vision

## Slide 2
Low-Altitude Perception: Demand and Constraints
2 / 14
Infrastructure inspection
Emergency response
Low-altitude economy
Autonomous aerial sensing
WHAT CONSTRAINS IT
1
Device
Onboard compute and power budgets are tight — full-capacity models do not fit.
2
Link
The air-to-ground uplink is narrow and fluctuates; the per-frame bit budget is not stable.
3
Environment
Dense haze scatters the visible band and erases small ground targets.
4
Cloud
Capacity is abundant — but only reachable through constraint 2.
VISIBLE VS. INFRARED AS HAZE INCREASES
Top: visible band — detections collapse as transmittance falls to 0.20.
Bottom: thermal infrared — the same targets persist. Source: paper Fig. 2(c).

## Slide 3
Why Neither Cloud-Only nor Edge-Only Works
3 / 14
Cloud-only
ship everything up, compute remotely
UAV
Cloud
+65.5 kbit/frame
✓
Full model capacity
✗
Second modality floods the uplink
✗
Transmission-bound latency
Edge-only
keep everything onboard
UAV
Cloud
✗
no uplink — but no capacity
✓
Lowest latency
✗
4 of 7 baselines exceed Orin Nano memory
✗
Fastest that fits still needs 128 ms/frame
Collaborative
decide at the edge, reconstruct in the cloud
UAV
Cloud
+6.6 kbit/frame
✓
Full capacity, on the cloud side
✓
Sparse, task-selected uplink
✓
Bounded latency under a weak link
How do we jointly optimise computation and communication?
Not “which dehazing model is best”, but: given a fixed number of bits per frame, which bits do you spend?
EVIDENCE · TABLE 1
Full-frame IR alone costs 65.5 kbit/frame — 65.5 ms at 1 Mbps, twice the 33.3 ms budget of a 30 fps stream.

## Slide 4
System Overview: The Collaborative Pipeline
Three stages under one contract — the edge decides where, the link carries only that, the cloud reconstructs in parallel.
4 / 14
EDGE · LINK · CLOUD
Edge decides where
VIS is the anchor stream; infrared is requested only where visible evidence has collapsed.
Link carries only that
A single H.26x track — IR pixels embedded in-band as SEI, with ROI cores ordered first.
Cloud reconstructs in parallel
Every ROI processed concurrently on GPU, then confidence-gated blending into the frame.

## Slide 5
Edge Side: Deciding What Deserves the Uplink
The edge does not compress the image — it performs selection, a far cheaper computation and a far larger bandwidth saving.
5 / 14
EDGE
Edge stage of the framework (paper Fig. 3, left panel)
THE SELECTION RULE, IN WORDS
Transmit infrared where the IR detector is confident and no visible detection overlaps it — that is, where infrared carries information the visible stream has already lost.
Δ = ŝ_IR · (1 − IoU_max) · transmit if Δ ≥ θ_diff and area ≥ A_min · tuned optimum θ_diff = 0.4, A_min = 576 px² (Table 5)
WHAT RUNS AT THE EDGE — AND WHY IT BELONGS THERE
Module | Cost profile | Why the edge
Lightweight VIS + IR detectors | small, fixed-cost inference | must see raw sensor data before encoding
Differential ROI criterion | arithmetic on box lists | needs both modalities co-located
Merge · stabilise · track IDs | negligible | keeps the payload temporally coherent
Encoder + in-band SEI packing | hardware codec | the bit decision belongs where bits originate
6.6 kbit
per frame — the only infrared that leaves the aircraft. The payload scales with the area of degraded regions, not with frame size.

## Slide 6
Communication-Efficient Transmission
Same restoration quality at roughly one tenth of the infrared uplink — the ratio, not the raw gain, is the contribution.
6 / 14
LINK
6.6 kbit
infrared payload per frame,
against 65.5 kbit for full-frame IR
− 89.9 %
infrared uplink volume
− 63.9 %
total per-frame uplink
THE COMMUNICATION–COMPUTATION TRADE-OFF IS MEASURED, NOT ASSERTED (VTUAV, Table 4)
Strategy | PSNR | mAP50 | Cloud time | IR uplink
VIS anchor only | 28.63 | 0.527 | 24 ms | 0
+ full-frame IR | 32.07 | 0.635 | 52 ms | 65.5 kbit
+ IR-ROI (ours) | 31.92 | 0.632 | 31 ms | 6.6 kbit
Give up 0.15 dB — 0.5 % — and buy 40 % of the cloud compute and 90 % of the infrared bits.

## Slide 7
Robustness When the Uplink Fluctuates
Bandwidth loss is modelled as prefix truncation — core-first scheduling keeps a truncated stream semantically useful.
7 / 14
LINK
VTUAV · SEI prefix truncation at three levels · four serialisation orders (Table 6)
COIS gains are largest where the link is worst: +8.5 % mAP50 at 70 % truncation, tapering to +3.0 % at 10 %.
Center-out spiral
Each ROI is serialised from its core outward, so the earliest bits carry the most informative pixels.
Interleaved across ROIs
Segments from all active ROIs are interleaved core-first, so no single region monopolises a short prefix.
Any prefix is useful
COIS leads at every truncation level and against every alternative order.

## Slide 8
Cloud Side: Capacity Where It Actually Pays Off
The cloud’s advantage is parallelism as much as capacity — that is what keeps the frame deadline.
8 / 14
CLOUD
Cloud stage of the framework (paper Fig. 3, right panel)
1
Scalable parallel execution
All ROIs of a frame run concurrently on GPU — cloud time falls from 52 ms (full-frame IR) to 31 ms.
2
Capacity the device cannot host
Cross-spectral alignment and attention that would not fit in onboard memory.
3
Three-stage processing
Align (coarse-to-fine displacement + confidence) → attend (inject IR residual where alignment is trusted) → aggregate (confidence-gated blending).
PIPELINED, SO THROUGHPUT IS max( · ) NOT sum( · )
Edge 26 ms
Cloud 31 ms
→ max(26, 31) = 31 ms ≤ 33.3 ms
Graceful degradation floor. If no infrared arrives — link outage, no ROI triggered, truncated payload — the pixel falls back to the visible anchor. Enhancement is additive, never load-bearing.

## Slide 9
What Actually Enables the Cooperation
Three mechanisms — each solving an edge–cloud systems problem.
9 / 14
1
Where to spend bits
PROBLEM
The uplink budget is smaller than the second modality.
MECHANISM
VIS–IR differential ROI selection — transmit infrared only where visible evidence has collapsed.
EVIDENCE
65.5 → 6.6 kbit/frame at −0.15 dB
Tables 4, 10
2
Surviving a fluctuating link
PROBLEM
Bits available per frame are not known in advance.
MECHANISM
ViStream-SEI with COIS — in-band single-track transport, ROI cores scheduled first.
EVIDENCE
+8.5 % mAP50 at 70 % truncation
Table 6
3
Fusing across a lossy boundary
PROBLEM
VIS and IR arrive misaligned in time and space.
MECHANISM
Confidence-gated cross-spectral fusion — align, gate, and fall back to the anchor when unsure.
EVIDENCE
+1.55 dB over HDCFN at 15 px shift
Table 9

## Slide 10
Experimental Validation Across Four System Axes
Validated as a system — quality, communication, computation and a real aircraft — not only as an image-quality benchmark.
10 / 14
① ③ QUALITY–COST FRONTIER · VTUAV, 7 baselines
+1.86 dB PSNR over the best baseline · −49 % parameters · 4.9× faster on the edge device
② COMMUNICATION EFFICIENCY
−89.9 % infrared uplink · +8.5 % mAP50 at 70 % truncation
① DOWNSTREAM PERCEPTION · YOLOv8m on VTUAV
Metric | HDCFN | Ours | Gain
mAP50 | 0.581 | 0.632 | +8.8 %
mAR50 | 0.656 | 0.702 | +7.0 %
The recall gain is the meaningful one — fewer missed small, low-contrast targets.
④ REAL AIRCRAFT, REAL WEATHER
hazy input → ours
Zenmuse H20T UAV · ~15,000 real VIS–IR frames · best NIQE 15.70 / PIQE 34.89

## Slide 11
Deployment Concept: Cloud–Network–Edge Inspection
11 / 14
Architectural positioning — not evaluated in the paper. The paper models uplink at 1–3 Mbps citing an LTE–UAV feasibility study; it runs no 5G field trial, no end-to-end glass-to-glass latency measurement, and no multi-UAV scheduling evaluation.
UAV sensing
VIS + IR capture
Edge gateway
ROI selection, in-band packing
26 ms/frame, Orin-class device
Mobile network
uplink-constrained bearer
payload shaped to 1–3 Mbps
Cloud AI platform
ROI-parallel enhancement
31 ms/frame on GPU
Decision support
defect and hazard detection,
alerting, archival
Standards-compatible transport
The infrared payload rides as user_data_unregistered SEI inside a single H.26x track. No second stream, no bespoke protocol, no change to the bearer — it traverses ordinary video infrastructure.
Degradation is graceful, not cliff-edged
Bandwidth loss costs enhancement quality, never stream integrity. The visible anchor always survives, so the analytics pipeline never goes dark.
WHAT THIS WORK CONTRIBUTES AT EACH LAYER
Layer | Operator asset | Contribution of this work
Aircraft / edge gateway | UAV + onboard compute (Orin-class) | 26 ms/frame selection stage — fits the device budget
Access network | mobile uplink bearer | payload shaped to a 1–3 Mbps budget; single standard video track
Cloud | GPU inference platform | ROI-parallel enhancement at 31 ms/frame

## Slide 12
Contributions: Computing, Communication, Intelligence
Three separable contributions — and it is worth being precise about which is which.
12 / 14
COMPUTING
system architecture contribution
Collaborative workload allocation
An asymmetric split: cheap, decisive selection at the edge; expensive, parallel reconstruction in the cloud — executed as a pipeline.
26 ms edge / 31 ms cloud
throughput = max( · ), not sum( · )
3.47 M parameters — lowest in the comparison
COMMUNICATION
communication efficiency contribution
ViStream-SEI with COIS
Single-track, in-band ROI transport whose any prefix is useful — and which needs no change to the bearer.
−89.9 % infrared uplink at −0.15 dB
+8.5 % mAP50 under 70 % truncation
standards-compatible H.26x SEI
INTELLIGENCE
algorithm contribution
Differential selection + gated fusion
Infrared used exactly where the visible band has failed, gated by cross-spectral alignment confidence.
+1.86 dB PSNR · +8.8 % mAP50
+7.0 % mAR50
robust to ±2-frame and 15-px misalignment
The system contribution is the ratio, not any single number: 0.5 % of quality for 90 % of the bits and 40 % of the cloud compute.

## Slide 13
Thanks for watching!