## Slide 1
Yafeng Yin1, Lei Xie1, Jie Wu2, Athanasios V. Vasilakos3, Sanglu Lu1
1State Key Laboratory for Novel Software Technology, Nanjing University, China
2Department of Computer and Information Sciences, Temple University, USA
3University of Western Macedonia, Greece
Focus and Shoot: Efficient Identification over
RFID Tags in the Specified Area
MobiQuitous 2013

## Slide 2
Motivation and Problem
1
Outline
Observations
2
Baseline Solutions
3
Our Solutions
4
Evaluation and Conclusion
5
1

## Slide 3
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
2
Scenario
Warehouse Management
Sampling Inspection
 How to efficiently identify the tags in the specified area ?
In these kinds of applications, in order to have a good knowledge of the tags in the specified area, we need to identify as many tags as possible in the area efficiently.

## Slide 4
System Model
 Efficient tag identification in the specified area in the realistic environments.
Tag Identification;
Specified area;
Realistic environments;
target tags
interference tags
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
3

## Slide 5
System Model
Antenna is rotatable.
Power is adjustable.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
4

## Slide 6
Problem Description
Number of target tags in the specified area: m
Number of identified target tags: s
Number of identified interference tags: u
Efficient tag Identification in the specified area:
Identify as many target tags as possible while minimize the execution time.
 1) Constraint: Coverage ratio, ≥ α
2) Objective: Minimize execution time T
Misreading ratio: , which is related to T.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
5

## Slide 7
Challenge
target tags
interference tags
(1) Make the antenna face towards the specified area;
(2) How to find the boundary of the area?
How to efficiently focus on the specified area ?
(3) How to select the optimal power ?
Realistic environments:
Interference;
Energy absorption;
Multipath effect…
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
6

## Slide 8
Observations from the realistic environments
Angle between the antenna and the tag
1) As the angle between the radiation direction and the surface of the antenna decrease,
the reading performance decreases.
2) When a tag is located in the center of the interrogation region, the reader often has a
good reading performance, no matter how the tag is placed.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
7

## Slide 9
Observations from the realistic environments
Angle between the antenna and the tag
1) As the angle between the radiation direction and the surface of the antenna decrease,
the reading performance decreases.
2) When a tag is located in the center of the interrogation region, the reader often has a
good reading performance, no matter how the tag is placed.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
8

## Slide 10
Observations from the realistic environments
Reader's Power
1) The larger the reader’s power, the larger the interrogation region.
2) As the power increases, the new identified tags may not be located in the boundary.
3) If a tag can be identified with a low power, it must be identified with a larger power.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
9

## Slide 11
Observations from the realistic environments
Distance between the tags and the antenna
1) As the distance of the tags and the antenna increases, the reading performance decreases.
2) When the distance and the tags are fixed, the maximum converge ratio has an upper bound.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
10

## Slide 12
Observations from the realistic environments
Effect of Tag Size
1) The tag size can affect the effective interrogation region.
2) The tag size has little effect on the number of identified tags.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
11

## Slide 13
Indication from the realistic environments
When the distance between the tags and the antenna is fixed, the distribution of tags is fixed, the converge ratio has an upper bound (Depend on the realistic Environments).
If we want to improve the reading performance, we should make the objects be located in the center of the interrogation region.
Since the tag size has little effect on the number of identified tag, we can find the boundary of the specified area by identifying some tags around the area.
When we need to focus on a specified area, we need to select an optimal power.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
12

## Slide 14
Baseline Solutions
Identification with Maximum Power
In order to identify as many target tags as possible:
The solution uses the maximum power to identify the tags.
Identification with the maximum power.
The effective interrogation region is too large.
Weakness:
1) More misreading ratio;
2) More execution time.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
13

## Slide 15
Baseline Solutions
Identification with Minimum Power
In order to only focus on the specified area (not identify the interference tags):
The solution uses the minimum power to identify the tags.
 It needs to rotate the antenna to scan all the target tags.
Weakness:
1) Multiple scans;
2) Low converge ratio;
3) More execution time
The effective interrogation region is too small.
Identification with the minimum power.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
14
How to make the interrogation region just enough to cover the area ?

## Slide 16
Photography based tag Identification with Distance measurement (PID)
The process of PID can be compared to the picture-taking process in a camera.
—— 1) Focusing Process: focus on the specified area (area A) with a 3D camera;
—— 2) Shooting Process: collect the tag IDs in the interrogation region.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
15

## Slide 17
Photography based tag Identification with Distance measurement (PID)
Focusing Process
The process of PID can be compared to the picture-taking process in a camera.
—— 1) Focusing Process: focus on the specified area (area A) with a 3D camera;
—— 2) Shooting Process: collect the tag IDs in the interrogation region.
1) The antenna rotates towards the center of the specified area A with a 3D camera;
2) The reader adjusts the power to make its scanning range just enough to cover the area A：
—— Establishing the boundary;
—— Power Stepping;
The distance between the tags and the antenna is fixed.
The distribution of tags is unknown.
 We can only adjust the antenna’s angle and the reader’s power.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
16

## Slide 18
Photography based tag Identification with Distance measurement (PID)
Focusing Process
1) Establishing the boundary:
Although the specified area A is appointed by a 3D camera, the reader can hardly find
the boundary of the area.
 Outline the specified area.
1) Identify a part of interference tags in the boundary:
2) Use these tags as reference tags of the boundary.
Minimum interval
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
17
, represents the number of tags that should be steadily identified, in order to describe the boundary.

## Slide 19
Photography based tag Identification with Distance measurement (PID)
Focusing Process
2) Power Stepping:
Adjust the reader’s power to make its scanning range be just enough to cover the area A.
 Find optimal power to just enough cover the area A.
2) Update reader’s power:
3) Identify tags in the boundary:
—— When , optimal power
1) Choose the minimum active power ;
, is related to the realistic environments,
while can be derived from the value coverage ratio.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
18

## Slide 20
Photography based tag Identification with Distance measurement (PID)
Shooting Process
ID1, ID2, ID3, …, IDn
IDi
Request message
We do not modify any parameter of the commercial reader (Alien-9900+), which conforms
to EPC C1G2 Standard.
Objective: Collecting the tag IDs in the interrogation region.
Approach: —— Identifying one tag ID in each slot.
—— Only no tags respond to reader, the process terminates, which means
each tag has transmitted its tag ID to the reader.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
19

## Slide 21
Photography based tag Identification with Angle rotation (PIA)
Identify the target tags without any auxiliary equipment.
Focusing Process
1) Exploring the boundary:
Rotate the antenna to explore the boundary of the specified area.
 Outline the specified area.
1) Identify a part of target tags:
2) Identify some interference tags Nl (Nr) of the boundary by rotating ( ) to left (right);
3) Use the tags identified with smaller angle as the reference tags of the boundary.
Smaller angle
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
20
and .
The remaining process is the same as that in PID.

## Slide 22
Performance Evaluation
System Prototypes
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
21
d
Minimum Interval: l
d
Minimum Interval: l
The center box is the specified area.
The number of target tags in the specified area is s.
The number of interference tags out of the specified area is u.
We get α=60% and based on the realistic environments. We vary s, u, d, l to
evaluate the performance of each solution.
Performance Metrics: Execution time, coverage ratio, misreading ratio.

## Slide 23
Performance Evaluation
We set d=1m, l=1m, s=80, u=70 by default.
Coverage Ratio
PID, PIA, and MaxPw can satisfy the requirement of coverage ratio.
MinPw can not satisfy the requirement because of its power is too small.
 We ignore MinPw in the following comparisons.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
22

## Slide 24
Performance Evaluation
We set d=1m, l=1m, s=80, u=70 by default.
Execution Time
PID and PIA have better performances than MaxPw.
When s=120, PID can reduce T by 46% compared to MaxPw.
When u=270, PID can reduce T by 84.5% compared to MaxPw.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
23

## Slide 25
Performance Evaluation
We set d=1m, l=1m, s=80, u=70 by default.
Misreading Ratio
PID and PIA have lower misreading ratios that MaxPw, because PID and PIA only focus
on the specified area and use the optimal power.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
24

## Slide 26
Conclusion
—— We investigate the problem of tag identification in the specified area.
—— We conduct extensive experiments on the commodity RFID systems.
—— We propose the photography based identification method, which works in a similar way of picture-taking in a camera.
Based on the picture-taking scheme, we propose two solutions PID and PIA.
1) PID works with a 3D camera;
2) PIA works without any auxiliary equipment.
—— Realistic environments show that our solutions outperform the baseline solutions.
Motivation and Problem
Evaluation and Conclusion
Observations
Baseline Solutions
Our Solutions
25

## Slide 27
Thank you !
Questions ?
MobiQuitous 2013