## Slide 1: Dynamic Mobile Charger Scheduling in Heterogeneous Wireless Sensor Networks
Hua Huang, Shan Lin, Lin Chen, Jie Gao, Anwar Mamat, Jie Wu
Presenter: Hua Huang
2 Univ. Paris-Sud 11
3 University of Maryland College Park
4 Temple University
1 Stony Brook University

## Slide 2: Problem Description
Network Model
  Sensor set:, mutual distance matrix:
  battery capacity: , energy consumption rate:
Charger Model
  single mobile charger
  zero charging time
Optimization Goal
  Coverage Ratio
  Energy Storage

## Slide 3: Problem Formulation
Maximizing a convex function, discrete constraints
NP complete
  proved by reducing the Traveling Salesman Problem ( TSP) to it

## Slide 4: Related Work
Zhang, Sheng, Jie Wu, and Sanglu Lu. "Collaborative mobile charging for sensor networks." Mobile Adhoc and Sensor Systems (MASS), 2012 IEEE 9th International Conference on. IEEE, 2012.
He, Liang, et al. "Esync: An energy synchronized charging protocol for rechargeable wireless sensor networks." Proceedings of the 15th ACM international symposium on Mobile ad hoc networking and computing. ACM, 2014.
Xie, Liguang, et al. "On traveling path and related problems for a mobile station in a rechargeable sensor network." Proceedings of the fourteenth ACM international symposium on Mobile ad hoc networking and computing. ACM, 2013.

## Slide 5: Challenge
Shortest Route (TSP) Scheduler
  charges along shortest route
  Fail to consider about node urgency

## Slide 6: Challenge
Earliest Deadline First (EDF) Scheduler
  charges most urgent node
  Fail to consider about traveling cost

## Slide 7: Challenge
Both traveling cost and node urgency are essential

## Slide 8: Spatial Dependent Model
Cluster Dependency:
  When charging i, traveling costs for nearby nodes are reduced.
Path Dependency:
  When traveling to i, nodes near the path are recharged without much detour

## Slide 9: Spatial Dependent Task (SDT) Scheduler
Idea:
  Searches for the most urgent node cluster
  charges nearby nodes along the path
Solution Overview
  Search the cluster to recharge
  Construct the directed acyclic travel graph
  Searches for the route to travel using critical path algorithm

## Slide 10: Spatial Dependent Task (SDT) Scheduler
Cluster Priority:
Path Priority:
Distance
detour cost
Weighted sum of urgency
Extra gain

## Slide 11: Spatial Dependent Task (SDT) Scheduler (cont’d)
Traveling graph definition
Given the distance
Directed Edge exists if:
<

## Slide 12: Evaluation
Baseline algorithms
  Shortest Route (TSP) scheduler
  Earliest Deadline First (EDF) scheduler
  Maximum Response Ratio First (MRF) scheduler
  EDF with node insertion (EDF-I)
Simulation set-up
  energy consumption rate modeling real traces
  225 nodes in square area
  different sizes and workloads

## Slide 13: Evaluation
Influence of work loads
SDT performs well when energy consumption rates
  3 clusters, SDT10% better than TSP, 5% better than EDF

## Slide 14: Evaluation
SDT degrades gracefully. 5% better than EDF
TSP performs well when network area 4% better than others

## Slide 15: Evaluation (cont’d)
Trade-off between traveling time and urgency
SDT scheduler spends most of the time charging urgent nodes

## Slide 16: Conclusion
Problem Definition
  Models and optimization goal
Challenge
  NP-Complete
  Consider both Spatial and temporal constraints
SDT Scheduler
  Select cluster
  Search best path
Evaluation
  SDT scheduler Achieves better performance
  TSP works well in large networks

## Slide 17: Future Work
Design algorithms with performance bounds

## Slide 18
Questions?