## Slide 1: Efficient Switch Migration for Controller Load Balancing in Software Defined Networking
Rajorshi Biswas and Jie Wu
Dept. of Computer and Info. Sciences
Temple University

## Slide 2: Outline
Switch migration and System Model
Some existing works
Problem Definition: Minimizing Cost
Different solutions
Simulation and Experimental results
Q&A
Notes: This is the outline of my talk

## Slide 3: System Model
Switch Migration
  Changing the controller of an SDN switch
Controller Load
  Path finding requests
  Intermediate node query requests
Response Delay:
  # of hops to controller
  Controller load
Green Flow
  path construction (A) + intermediate query (D)
Red Flow
  path construction (X) + path construction (D) + intermediate query (B)

## Slide 4: Switch Migration is Challenging
Challenges
  Sporadic assignment leads to higher number of path construction.
  Flows change frequently.
  Live migration is not possible.

## Slide 5: Previous Works
Systems | Limitations
ILP based Systems: X. Zhang, L. Li and C. -b. Yan, "Robust Controller Placement Based on Load Balancing in Software Defined Networks," ICNSC, 2020 L. Li, N. Du, H. Liu, R. Zhang and C. Yan, "Towards robust controller placement in software-defined networks against links failure," 2019 IFIP/IEEE Symposium on Integrated Network and Service Management. | ILP based solutions takes long time in large topologies. Does not consider dynamic/incremental adjustment.
Heuristic/Greedy F. He and E. Oki, "Load Balancing Model against Multiple Controller Failures in Software Defined Networks," ICC 2020. | Does not consider the control network delay. Dynamic/incremental adjustments is not considered.

## Slide 6: Problem: Minimize Cost of Assignment
Cost is a weighted sum of three metrics
  number of path construction request to
  number of intermediate query requests to .
  total number of hops from each switch to
Problem:
  Find a Switch-Controller Assignment that minimizes cost.
Constraints:
  Controller capacity constraints
  Switch migration can be only to neighbors
Two Scenarios:
  Initial deployment
    Greedy
    Clustering
  Incremental deployment
    Greedy
NP-Hard, Graph Partitioning Problem

## Slide 7: Initial deployment: Minimize Cost
Greedy Solution:
  Consider a bucket for each controller.
  Initially, add the switch to the bucket which produce minimum amount of cost.
  Consider the neighbors for future extension.
  Add a switch from the neighbors that produce minimum cost.
Complexity:
Notes: Usually, W1 is 10 times of W2

## Slide 8: Initial deployment: Minimize Cost
An Example:
First round:
  [A] [W]
  Candidates [B, C, D] [B, X, Y]
  C-> is the minimum cost
Second round:
  [A, C] [W]
  Candidates [B,D] [B, X, Y]
Final Round:
  [A,B,C,D,X] [W,Y,Z]
Notes: Usually, W1 is 10 times of W2

## Slide 9: Initial deployment: Minimize Cost
Clustering Solution:
  Create distance matric from the topology
  This distance matrix is normalized and used for hierarchical clustering.
  We set the number of clusters as the number of controller.
  Each cluster is assigned to the controller that produces minimum cost.
Complexity:
Example:
  [A,B,C,D,X] [W,Y,Z]
Notes: Usually, W1 is 10 times of W2

## Slide 10: Incremental Deployment
Problem:
  Find a Switch-Controller Assignment that minimizes cost.
Constraints
  Controller capacity constraints
  Old switch assignment-new switch assignment < K
  Switch migration can be only to neighbors

## Slide 11: Incremental Deployment Solution
Greedy:
  Find overloaded and underutilized controllers.
  Find the neighbors of that belongs to
  Calculate the benefit of migration for each neighbors.
  Choose the neighbors with max benefit.
  Continue K times or until every is balanced.
Complexity:
overloaded
underutilized
Migration of X is more beneficiary than migration of B

## Slide 12: Experiments and Simulations
Migration delay: 5.2s
Sparse T1
Dense T2

## Slide 13: Simulation Results
Initial Deployment:
Distance based has the highest cost
Greedy is 10% lower and
Clustering is 20% lower than distance based
Incremental Deployment:
Distance based has the highest cost
10 updates is 11% lower and
20 updates is 24% lower than distance based
Sparse T1
Dense T2

## Slide 14: Thank You
Q&A