## Slide 1: Adaptive Backbone-based Routing in Delay Tolerant Networks
Shuhui Yang Jie Wu
Math, Computer Science, and Statistics Dept. Computer and Information Science Dept. Purdue University Calumet Temple University
IEEE MASS 2013, Hangzhou, China

## Slide 2: Outline
Introduction
Preliminaries
Problem Formulation
  Network model
  A delay-tolerant network backbone
  The delay-tolerant connected dominating set (DTCDS)
Localized Heuristic Solution for DTCDS
Discussion
Simulation Results
Conclusion & Future Work

## Slide 3: Introduction
Delay/Disruption tolerant networks (DTNs)
  Support interoperability
  Tolerate delay and disruption
  Intermittent/Scheduled/opportunistic communication links
DTN-oriented routing
  New problem
  Challenges: mobile, power-limited, intermittently-available links
  Also help to provide off-loading for centralized wireless communication
Node mobility in DTNs
  Large scale movement causes disconnection
  Realizes message delivery
    “store-carry-forward” mode adopted

## Slide 4: DTN Routing
Categories
  Deterministic routing
  History or predication-based routing
  Epidemic routing
Rational
  For most DTNs, node mobility is not entirely random
    Carried by human beings
Promising solution
  Aggregate contacts in the past
  Use social graph
  Predict future contact likeliness
  Use metrics from complex network analysis
  Make forwarding decisions

## Slide 5: In this work
Design a modeling approach for DTNs
  Weighted graph derived
Put forward the concept of a delay-tolerant network backbone
  Used for message forwarding in DTNs
Develop the delay-tolerant connected dominating set (DTCDS) concept and problem
  To approximate the delay-tolerant network backbone
Propose heuristic localized solutions
  to the minimum equally effective DTCDS problem
Study the performance of the proposed methods

## Slide 6: Preliminaries
Routing in DTNs
  Epidemic routing (blind flooding)
    No prediction
    Optimal latency
    Large buffer capacity
  Deterministic routing
    Network movement is (partially) scheduled
    The shortest path can be calculated
    Node trajectory is designable to assist routing performance
  In between
    Use past information to predict future movements
    Each node makes a decision upon each received message: cost expensive
  Proposed work
    Use past information to derive a weighted graph, and
    Form a network “backbone” for message forwarding, to
    Limit the copies of messages & provide a latency guarantee

## Slide 7: Preliminaries
Connected dominating set (CDS)
  In mobile ad hoc networks (MANETs) and wireless sensor networks (WSNs)
  Used to approximate a virtual network backbone
  Each node is either in the CDS or has a one-hop neighbor in the set
  Minimum CDS: NP-complete
CDS construction
  Localized approach
    Local h-hop information
    No propagation
  Existing algorithms
    Marking process
    Rule k
    Coverage condition

## Slide 8: Network Model
A DTN with n nodes,
  : meeting frequency (MF)
  : expected data delivery latency
  : the expected data delivery latency
  of path
Derived weighted graph for a DTN
  A time-space model
  : no link between nodes

## Slide 10: Delay Tolerant Network Backbone
A subset of nodes in the derived weighted graph
  Each node can send a message to any other node
  Only nodes in the backbone will forward messages
  Note: forwarding is not broadcasting
Design goals
  Efficiency
    small backbone to limit message copies
  Effectiveness
    expected end-to-end delay is bounded

## Slide 11: The Delay Tolerant Connected Dominating Set (DTCDS)
A subset of the DTN graph, such that
  The subsets are connected among themselves
  Every non-selected node has at least one selected node as a neighbor
DTCDS is the same with CDS
A smaller DTCDS is desired

## Slide 12: The Minimum Equally Effective DTCDS
The DTCDS
  With the smallest number of selected nodes
  The expected delivery latency between any two nodes is the same with that when all nodes forward messages
  Traditional CDS: 1, 2
  Minimum Equally Effective
  DTCDS: 1, 2, 6

## Slide 13: Localized Heuristic Solution
Accumulated delivery latency
  Inspired by the flow network concept
  The meeting frequency of two nodes via different paths can be added
  With d node disjoint paths connecting two nodes:

## Slide 14: Localized Heuristic Solution
Accumulated Node Coverage Condition (ANCC)
  A node, v, is withdrawn from the DTCDS if, for any two neighbors of it, u and w, a group of disjoint path exists, such that
    Each intermediate node on any path has a higher priority than node v, and
    The accumulated delivery latency of the group of paths is smaller than or equal to the delivery latency of path u, v, w.

## Slide 15: Localized ANCC algorithm

## Slide 16: Discussion
Routing with only marked nodes by ANCC forwarding has the same performance as routing with all nodes forwarding, in terms of message delay
The ANCC algorithm is adaptive
  Smaller forwarding node set with more accumulated knowledge on nodes’ contacts
  Existing DTN routing can be applied to ANCC to reduce forwarding when there is no optimal latency requirement
  ANCC can be relaxed to achieve a smaller forwarding set with an acceptable increased latency
    The accumulated delivery latency of the group of paths is smaller than or equal to k times the delivery latency of path u, v, w.
  When deriving the graph with the weight being contact probability, the forwarding set generated by ANCC guarantees an optimal end-to-end delivery ratio

## Slide 17: Simulation
Adjustable parameters
  Number of nodes n: 20~160
  Average node degree d: 6, 18, 30
  Number of hops of local information h: 2, 3, 4
  Range of meeting frequency for weight assignment r: 10, 50, 100
  Relaxation factor k: 1, 2, 3
Performance metrics
  The size of the forwarding node set
  Expected average message delivery latency

## Slide 19: Simulation Summary
Forwarding set size
  ANCC reduces the size of forwarding set by 50% to 80%, with different graph densities
  More local information helps to reduce the size
  A graph being more dense helps to reduce the size
The expected delivery latency
  when k is 2, it is 1.5 times of that of the optimal solution, and
  2 times that of when k is 3

## Slide 20: Conclusion & Future Work
A modeling method for DTNs
A concept of delay-tolerant network backbone
  Reduced number of message copies
  Optimal performance in terms of end-to-end delay
A formalized minimum equally-effective delay-tolerant connected dominating set problem
  Approximate delay-tolerant network backbone
A heuristic localized algorithm
Future work: consider more realistic system settings, limited buffer size, etc.

## Slide 21: Questions?
Thank you!